## Slide 1: Lecture 05: Assembly Language Programming (2)

## Slide 2
The 80x86 IBM PC and Compatible Computers
Chapter 3
Arithmetic & Logic Instructions and Programs
Chapter 6
Signed Numbers, Strings, and Tables

## Slide 3: Arithmetic Instructions
Addition
Subtraction
Multiplication
Division

## Slide 4: Unsigned Addition
ADD dest, src ;dest = dest + src
  Dest can be a register or in memory
  Src can be a register, in memory or an immediate
  No mem-to-mem operations in 80X86
  Change ZF, SF, AF, CF, OF, PF
ADC dest, src ;dest = dest + src +CF
  For multi-byte numbers
  If there is a carry from last addition, adds 1 to the result

## Slide 5: Addition Example of Individual Bytes
Draw the layout of the data segment in memory
What’s this for?

## Slide 6: Addition Example of Multi-byte Nums

## Slide 7: Unsigned Subtraction
SUB dest, src ;dest = dest - src
  Dest can be a register or in memory
  Src can be a register, in memory or an immediate
  No mem-to-mem operations in 80X86
  Change ZF, SF, AF, CF, OF, PF
SBB dest, src ;dest = dest - src – CF
  For multi-byte numbers
  If there is a borrow from last subtraction, subtracts 1 from the result

## Slide 8: Subtraction Example of Individual Bytes
CPU carries out
  take the 2’s complement of the src
  add it to the dest
  invert the carry
CF = 0: positive result ;
CF = 1: negative result in 2’s complement
  Magnitude: NOT + INC

## Slide 9: Subtraction Example of Multi-byte Nums

## Slide 10: Unsigned Multiplication
MUL operand
byte X byte:
  One implicit operand is AL, the other is the operand, result is stored in AX
word X word:
  One implicit operand is AX, the other is the operand, result is stored in DX & AX
word X byte:
  AL hold the byte, AH = 0, the word is the operand, result is stored in DX & AX;

## Slide 11: Unsigned Multiplication Example

## Slide 12: Unsigned Division
DIV denominator
  Denominator cannot be zero
  Quotient cannot be too large for the assigned register
byte / byte:
  Numerator in AL, clear AH; quotient is in AL, remainder in AH
word / word:
  Numerator in AX, clear DX; ; quotient is in AX, remainder in DX
word / byte:
  Numerator in AX; quotient is in AL (max 0FFH), remainder in AH
double-word / word:
  Numerator in DX, AX; quotient is in AX (max 0FFFFH), remainder in DX
  Denominator can be in a register or in memory

## Slide 13: Unsigned Division Example

## Slide 14: Logic Instructions
AND
OR
XOR
NOT
Logical SHIFT
ROTATE
COMPARE

## Slide 15: AND
AND dest, src
  Bit-wise logic
  dest can be a register, in memory

## Slide 16: OR
OR dest, src
  Bit-wise logic
  dest can be a register, in memory

## Slide 17: XOR
XOR dest, src
  Bit-wise logic
  dest can be a register, in memory

## Slide 18: NOT
NOT operand
  Bit-wise logic
  dest can be a register or in memory
  X NOT X
  -------------------------------------------
  1 0
  0 1

## Slide 19: Logical SHIFT
SHR dest, times
  dest can be a register or in memory
  0->MSB->…->LSB->CF
  Times = 1:
  SHR xx, 1
  Times >1:
  MOV AL, times
  SHR xx, AL
SHL dest, times
  All the same except in reverse direction

## Slide 20: Example: BCD & ASCII Numbers Conversion
BCD: Binary Coded Decimal
  Digits 0~9 in binary representation
  Unpacked, packed
ASCII
  Code for all characters that you can read or write
  Digit characters ‘0’~’9’

## Slide 21: ASCII -> Unpacked BCD Conversion
Simply remove the higher 4 bits “0011”
E.g.,
asc DB ‘3’
unpack DB ?
-------------------------
MOV AH, asc
AND AH, 0Fh
MOV unpack, AH

## Slide 22: ASCII -> Packed BCD Conversion
First convert ASCII to unpacked BCD
Then, combine two unpacked into one packed
E.g., asc DB ‘23’
unpack DB ?
-------------------------
MOV AH, asc
MOV AL, asc+1
AND AX, 0F0Fh
MOV CL, 4
SHL AH, CL
OR AH, AL
MOV unpack, AH

## Slide 23: ROTATE
ROR dest, times
  dest can be a register, in memory
  Times = 1:
  ROR xx, 1
  Times >1:
  MOV AL, times
  ROR xx, AL
ROL dest, times
  All the same except in reverse direction

## Slide 24: ROTATE Cont.
RCR dest, times
  dest can be a register, in memory
  Times = 1:
  RCR xx, 1
  Times >1:
  MCV AL, times
  RCR xx, AL
RCL dest, times
  All the same except in reverse direction

## Slide 25: COMPARE of Unsigned Numbers
CMP dest, src
  Flags affected as (dest – src)
  E.g., CMP AL, 23
  JA lable1 ; jump if above, CF = ZF = 0

## Slide 27: COMPARE of Signed Numbers
CMP dest, src
  Same instruction as the unsigned case
  but different understanding about the numbers and therefore different flags checked

## Slide 29: Quiz
Given the ASCII table, write an algorithm to convert uppercase letters into lowercase letters and implement your algorithm using 86 assembly language