## Slide 1: Cortex-M3 Instruction Sets

## Slide 2
Chapter 4 in the reference book

## Slide 3
8.5 Instruction Sets
8.5.1 Assembly Basics
8.5.1.1 Assembler Language: Basic Syntax
In assembler code, the following instruction formatting is commonly used :
label: opcode operand1, operand2,... ; Comments
The label is optional, used to determine the address of the instruction.
The opcode is the instruction.
The number of operands in an instruction depends on the type of instruction.
  Normally, the first operand is the destination of the operation
The text after each semicolon (;) is a comment.
Note: the assembler syntax depends on which assembler tool you are using. Here we introduce the ARM assembler syntax.

## Slide 4
Example:
MOV R0, #0x12 ; Set R0 = 0x12 (hexadecimal)
MOV R1, #‘A’ ; Set R1 = ASCII character A
Immediate data are usually in the form #number
Define constants using EQU:
NVIC_IRQ_SETEN0 EQU 0xE000E100
NVIC_IRQ0_ENABLE EQU 0x1
...
LDR R0, =NVIC_IRQ_SETEN0 ; LDR here is a pseudo instruction that
; convert to a PC relative load by
; assembler.
MOV R1, #NVIC_IRQ0_ENABLE ; Move immediate data to register
STR R1, [R0] ; Enable IRQ 0 by writing R1 to address
; in R0

## Slide 5
Use DCB and DCD to define byte-size and word-size variables:
Example:
LDR R3, =MY_NUMBER ; Get the memory address value of MY_NUMBER
LDR R4, [R3] ; Get the value code 0x12345678 in R4
...
LDR R0,=HELLO_TXT ; Get the starting memory address of HELLO_TXT
BL PrintText ; Call a function called PrintText to display string
...
MY_NUMBER
DCD 0x12345678
HELLO_TXT
DCB “Hello\n”,0 ; null terminated string

## Slide 6
8.5.1.2 Assembler Language: Unified Assembler Language
UAL was developed to
  allow selection of 16-bit and 32-bit instructions
  make it easier to port applications between ARM code and Thumb code
The traditional Thumb syntax can still be used
Example:
ADD R0, R1 ; R0 = R0 + R1, using Traditional Thumb syntax
ADD R0, R0, R1 ; Equivalent instruction using UAL syntax
Note: with traditional Thumb instruction syntax, some instructions automatically change the flags in APSR; however, when the UAL syntax is used, whether the instruction changes the flag depends on the S suffix, e.g., ADDS R0, R0, R1

## Slide 7
With UAL, you can explicitly specify whether a Thumb or a Thumb-2 instruction you want by adding suffixes
Example:
ADDS R0, #1 ; Use 16-bit Thumb instruction by default for smaller size
ADDS.N R0, #1 ; Use 16-bit Thumb instruction (N=Narrow)
ADDS.W R0, #1 ; Use 32-bit Thumb-2 instruction (W=wide)
Note: In most cases, applications will be coded in C, and the C compilers will use 16-bit instructions if possible due to smaller code size

## Slide 8
32-bit Thumb-2 instructions can be half word aligned
Example:
0x1000 : LDR r0,[r1] ; a 16-bit instructions (occupy 0x1000-0x1001)
0x1002 : RBIT.W r0 ; a 32-bit Thumb-2 instruction (occupy 0x1002- ; 0x1005)
Most of the 16-bit instructions can only access registers R0 to R7
32-bit Thumb-2 instructions do not have this limitation

## Slide 9
8.5.2 Instruction List
16-Bit Data Processing Instructions
Instruction | Function
ADC | Add with carry
ADD | Add
AND | Logical AND
BIC | Bit clear (Logical AND one value with the logic inversion of another value)
CMN | Compare negative (compare one data with two’s complement of another data and update flags)
CMP | Compare (compare two data and update flags)
CPY | Copy (available from architecture v6; move a value from one high or low register to another high or low register)
LSL | Logical shift left
LSR | Logical shift right
MOV | Move (can be used for register-to-register transfers or loading immediate data)
MUL | Multiply

## Slide 10
MVN | Move NOT (obtain logical inverted value)
NEG | Negate (obtain two’s complement value)
ORR | Logical OR
ROR | Rotate right
SBC | Subtract with carry
SUB | Subtract
TST | Test (use as logical AND; Z flag is updated but AND result is not stored)
REV | Reverse the byte order in a 32-bit register (available from architecture v6)
SXTB | Signed extend byte (available from architecture v6)
SXTH | Signed extend half word (available from architecture v6)
UXTB | Unsigned extend byte (available from architecture v6)
UXTH | Unsigned extend half word (available from architecture v6)
(Continued)

## Slide 11
16-Bit Branch Instructions
Instruction | Function
B | Branch
B<cond> | Conditional branch
BL | Branch with link; call a subroutine and store the return address in LR
BLX | Branch with link and change state (BLX <reg> only)
CBZ | Compare and branch if zero (architecture v7)
CBNZ | Compare and branch if nonzero (architecture v7)
IT | IF-THEN (architecture v7)

## Slide 12
16-Bit Load and Store Instructions
Instruction | Function
LDR | Load word from memory to register
LDRH | Load half word from memory to register
LDRB | Load byte from memory to register
STR | Store word from register to memory
STRH | Store half word from register to memory
STRB | Store byte from register to memory
LDMIA | Load multiple increment after
STMIA | Store multiple increment after
PUSH | Push multiple registers
POP | Pop multiple registers

## Slide 13
Other 16-Bit Instructions
Instruction | Function
SVC | System service call
BKPT | Breakpoint; if debug is enabled, will enter debug mode (halted), or if debug monitor exception is enabled, will invoke the debug exception; otherwise it will invoke a fault exception
NOP | No operation
CPSIE | Enable PRIMASK (CPSIE i)/FAULTMASK (CPSIE f ) register (set the register to 0)
CPSID | Disable PRIMASK (CPSID i)/ FAULTMASK (CPSID f ) register (set the register to 1)

## Slide 14
32-Bit Data Processing Instructions
Instruction | Function
ADC | Add with carry
ADD | Add
ADDW | Add wide (#immed_12)
AND | Logical AND
ASR | Arithmetic shift right
BIC | Bit clear (logical AND one value with the logic inversion of another value)
BFC | Bit field clear
CMP | Compare (compare two data and update flags)
CLZ | Count lead zero
EOR | Exclusive OR
LSL | Logical shift left
LSR | Logical shift right
MLA | Multiply accumulate

## Slide 15
MSL | Multiply and subtract
MOV | Move
MVN | Move negative
MUL | Multiply
ORR | Logical OR
ORN | Logical OR NOT
RBIT | Reverse bit
REV | Byte reserve word
ROR | Rotate right register
RSB | Reverse subtract
RRX | Rotate right extended
SBFX | Signed bit field extract
SDIV | Signed divide
(Continued)

## Slide 16
(Continued)
SMLAL | Signed multiply accumulate long
SMULL | Signed multiply long
SSAT | Signed saturate
SBC | Subtract with carry
SUB | Subtract
SUBW | Subtract wide (#immed_12)
SXTB | Sign extend byte
TEQ | Test equivalent (use as logical exclusive OR; flags are updated but result is not stored)
TST | Test (use as logical AND; Z flag is updated but AND result is not stored)
UBFX | Unsigned bit field extract
USAT | Unsigned saturate
UXTB | Unsigned extend byte
UXTH | Unsigned extend half word

## Slide 17
32-Bit Load and Store Instructions
Instruction | Function
LDR | Load word data from memory to register
LDRB | Load byte data from memory to register
LDRH | Load half word data from memory to register
LDRSB | Load byte data from memory, sign extend it, and put it to register
LDRSH | Load half word data from memory, sign extend it, and put it to register
LDM | LDM Load multiple data from memory to registers
LDRD | LDRD Load double word data from memory to registers
STR | STR Store word to memory
STM | Store multiple words from registers to memory
STRD | Store double word data from registers to memory
PUSH | Push multiple registers
POP | Pop multiple registers

## Slide 18
32-Bit Branch Instructions
Other 32-Bit Instructions
Instruction | Function
B | Branch
BL | Branch and link
TBB | Table branch byte; forward branch using a table of single byte offset
TBH | Table branch half word; forward branch using a table of half word offset
Instruction | Function
LDREX | Exclusive load word
STREX | Exclusive store word

## Slide 19
(Continued)
CLREX | Clear the local exclusive access record of local processor
MRS | Move special register to general-purpose register
MSR | Move to special register from general-purpose register
NOP | No operation
SEV | Send event
WFE | Sleep and wake for event
WFI | Sleep and wake for interrupt
ISB | Instruction synchronization barrier
DSB | Data synchronization barrier
DMB | Data memory barrier

## Slide 20
8.5.3 Instruction Descriptions
8.5.3.1 Assembler Language: Moving Data
Data transfers can be of one of the following types:
1. Moving data between register and register
2. Moving data between memory and register
3. Moving data between special register and register
4. Moving an immediate data value into a register

## Slide 21
MOV: move data between registers or immediate data to register
  e.g., MOV R8, R3; R3->R8
  MVN (move negative)
Load and Store: Load transfers data from memory to registers, and Store transfers data from registers to memory
Example | Description
LDRB Rd, [Rn, #offset] | Read byte from memory location Rn + offset
LDRH Rd, [Rn, #offset] | Read half-word from memory location Rn + offset
LDR Rd, [Rn, #offset] | Read word from memory location Rn + offset
LDRD Rd1,Rd2, [Rn, #offset] | Read double word from memory location Rn + offset
STRB Rd, [Rn, #offset] | Store byte to memory location Rn + offset
STRH Rd, [Rn, #offset] | Store half word to memory location Rn + offset
STR Rd, [Rn, #offset] | Store word to memory location Rn + offset
STRD Rd1,Rd2, [Rn, #offset] | Store double word to memory location Rn + offset

## Slide 22
Multiple Load and Store: LDM (Load Multiple); STM (Store Multiple).
Example | Description
LDMIA Rd!, <reg list> | Read multiple words from memory location specified by Rd. Address Increment After (IA) each transfer (16-bit Thumb instruction).
STMIA Rd!, <reg list> | Store multiple words to memory location specified by Rd. Address Increment After (IA) each transfer (16-bit Thumb instruction).
LDMIA.W Rd(!),<reg list> | Read multiple words from memory location specified by Rd. Address increment after each read (.W specified it is a 32-bit Thumb-2 instruction).
STMIA.W Rd(!), <reg list> | Write multiple words to memory location specified by Rd. Address increment after each read (.W specified it is a 32-bit Thumb-2 instruction).
LDMDB.W Rd(!), <reg list> | Read multiple words from memory location specified by Rd. Address Decrement Before (DB) each read (.W specified it is a 32-bit Thumb-2 instruction).
STMDB.W Rd(!), <reg list> | Write multiple words to memory location specified by Rd. Address Decrement Before each read (.W specified it is a 32-bit Thumb-2 instruction).

## Slide 23
“!” in the instruction MOV specifies whether the register Rd should be updated after the instruction is completed
Example:
STMIA.W R8!, {R0-R3} ; if R8 equals 0x8000, R8 changed to ; 0x8010 after store (increment by 4 words)
STMIA.W R8 , {R0-R3} ; R8 unchanged after store
Pre-indexing and Post-indexing:
Example:
LDR.W R0,[R1, #offset]! ; Read memory[R1+offset], with R1
; update to R1+offset
LDR.W R0,[R1], #offset ; Read memory[R1], with R1
; updated to R1+offset

## Slide 24
Usually a PUSH instruction will have a corresponding POP with the same register list, but this is not always necessary
PUSH {R0-R3, LR} ; Save register contents at beginning of subroutine
.... ; Processing
POP {R0-R3, PC} ; restore registers and return
Use the instructions MRS and MSR to access special registers
MRS R0, PSR ; Read Processor status word into R0
MSR CONTROL, R1 ; Write value of R1 into control register
Note: APSR can be accessed using normal instructions

## Slide 25
Moving immediate data into a register:
MOV R0, #0x12 ; Set R0 to 0x12, for data below 8 bits
MOVW.W R0,#0x789A ; Set R0 to 0x789A, for data over 8 bits but ; below 16 bits, using Thumb-2 instruction
MOVW.W R0,#0x789A ; Set R0 lower half to 0x789A
MOVT.W R0,#0x3456 ; Set R0 upper half to 0x3456. Now ; R0=0x3456789A
LDR (LDR pseudo-instruction, not the LDR instruction):
  A pseudo instruction provided in ARM assembler (not a real instruction) to load a register with either a 32-bit constant or an address
  LDR R0, =0x3456789A ; load an 32-bit constant
  LDR R0, =label+offset ; load an address
Where are immediate data?

## Slide 26
For Cortex-M3, if the address (i.e., value of a label) is a program address value, it will automatically set the LSB to 1 to indicate that it is Thumb code
LDR R0, =address1 ; R0 set to 0x4001
...
address1
0x4000: MOV R0, R1 ; address1 contains program code
...
If the address is a data address, LSB will not be changed.
LDR R0, =address1 ; R0 set to 0x4000
...
address1
0x4000: DCD 0x0 ; address1 contains data
...

## Slide 27
8.5.3.2 Assembler Language: Processing Data
Many data operation instructions can have multiple instruction formats.
Example: ADD
ADD R0, R1 ; R0 = R0 + R1
ADD R0, #0x12 ; R0 = R0 + 0x12
ADD.W R0, R1, R2 ; R0 = R1 + R2
When 16-bit Thumb code is used, an ADD instruction automatically changes the flags in the PSR.
32-bit Thumb-2 code can either change a flag or keep it unchanged
ADD.W R0, R1, R2 ; Flag unchanged
ADDS.W R0, R1, R2 ; Flag change

## Slide 28
Examples of Arithmetic Instructions
Instruction | Operation
ADD Rd, Rn, Rm ; Rd = Rn + Rm ADD Rd, Rm ; Rd = Rd + Rm ADD Rd, #immed ; Rd = Rd + #immed | ADD operation
ADC Rd, Rn, Rm ; Rd = Rn + Rm + carry ADC Rd, Rm ; Rd = Rd + Rm + carry ADC Rd, #immed ; Rd = Rd + #immed + carry | ADD with carry
ADDW Rd, Rn,#immed ; Rd = Rn + #immed | ADD register with 12-bit immediate value
SUB Rd, Rn, Rm ; Rd = Rn – Rm SUB Rd, #immed ; Rd = Rd – #immed SUB Rd, Rn,#immed ; Rd = Rn –#immed | SUBTRACT
RSB.W Rd, Rn, #immed ; Rd = #immed –Rn RSB.W Rd, Rn, Rm ; Rd = Rm - Rn MUL Rd, Rm ; Rd = Rd * Rm Multiply MUL.W Rd, Rn, Rm ; Rd = Rn * Rm | Reverse subtract Multiply
UDIV Rd, Rn, Rm ; Rd = Rn /Rm SDIV Rd, Rn, Rm ; Rd = Rn /Rm | Unsigned and signed divide
Refer to the reference book for other logical operation instructions and rotate and shift instructions. Then answer the question: why are there only rotate right operations but no rotate left operations?

## Slide 29
8.5.3.3 Assembler Language: Call and Unconditional Branch
The most basic branch instructions are:
B label ; Branch to a labeled address
BX reg ; Branch to an address specified by a register
Note: In BX instructions, the LSB of the value contained in the register determines the next state (Thumb/ARM) of the processor. In Cortex-M3, since it is always in Thumb state, this bit should be set to 1; otherwise, the program will cause a usage fault exception.
To call a function:
BL label ; Branch to a labeled address and save return address in LR
BLX reg ; Branch to an address specified by a register and
; save return address in LR.

## Slide 30
Branch using MOV, LDR and POP instructions
MOV R15, R0 ; Branch to an address inside R0
LDR R15, [R0] ; Branch to an address in memory location specified by R0
POP {R15} ; Do a stack pop operation, and change the program ; counter value to the result value.
Note:
1) also need to make sure that the LSB of the new program counter value is 0x1 (indicating the state of the next instruction is Thumb state)
2) BL instruction will destroy the content of LR. If you need the LR later, you should save the LR before using BL. For example, PUSH {LR}

## Slide 31
8.5.3.4 Assembler Language: Decisions and Conditional Branches
In the APSR, there are five flag bits; four of them are used for branch decisions.
Flag bits in APSR That Can Be Used for Conditional Branches
Flag | PSR Bit | Description
N | 31 | Negative flag (last operation result is a negative value)
Z | 30 | Zero (last operation result returns a zero value)
C | 29 | Carry (last operation returns a carry out or borrow)
V | 28 | Overflow (last operation results in an overflow)

## Slide 32
With combinations of the four flags (N, Z, C, and V), 15 branch conditions are defined.
Conditions for Branches or Other Conditional Operations
Symbol | Condition | Flag
EQ | Equal | Z set
NE | Not equal | Z clear
CS/HS | Carry set/unsigned higher or same | C set
CC/LO | Carry clear/unsigned lower | C clear
MI | Minus/negative | N set
PL | Plus/positive or zero | N clear
VS | Overflow | V set
VC | No overflow | V clear
HI | Unsigned higher | C set and Z clear
LS | Unsigned lower or same | C clear or Z set

## Slide 33
Example:
BEQ label ; Branch to address ‘label’ if Z flag is set
Thumb-2 version
BEQ.W label ; Branch to address ‘label’ if Z flag is set
(Continued)
LT | Signed less than | N set and V clear, or N clear and V set (N != V)
GT | Signed greater than | Z clear, and either N set and V set, or N clear and V clear (Z == 0, N == V)
LE | Signed less than or equal | Z set, or N set and V clear, or N clear and V set (Z == 1 or N != V)
AL | Always (unconditional) | —

## Slide 34
8.5.4 Several Useful Instructions in the Cortex-M3
8.5.4.1 MRS and MSR
Provide access to the special registers.
MRS <Rn>, <SReg> ; Move from Special Register
MSR <SReg>, <Rn> ; Write to Special Register
Special Register Names for MRS and MSR Instructions
Symbol | Description
IPSR | Interrupt status register
EPSR | Execution status register (read as zero)
APSR | Flags from previous operation
IEPSR | A composite of IPSR and EPSR
IAPSR | A composite of IPSR and APSR

## Slide 35
Example:
LDR R0, =0x20008000 ; new value for Process Stack Pointer (PSP)
MSR PSP, R0
EAPSR | A composite of EPSR and APSR
PSR | A composite of APSR, EPSR and IPSR
MSP | Main stack pointer
PSP | Process stack pointer
PRIMASK | Normal exception mask register
BASEPRI | Normal exception priority mask register
BASEPRI_MAX | Same as normal exception priority mask register, with conditional write (new priority level must be higher than the old level)
FAULTMASK | Fault exception mask register (also disables normal interrupts)
CONTROL | Control register
(Continued)
Note: Unless accessing the APSR, the MRS and MSR instructions can be used in privileged mode only.