## Slide 1: PCA9557: REMOTE 8-BIT I2C AND SMBus LOW-POWER I/O EXPANDER

## Slide 2
Reference Books
REMOTE 8-BIT I2C AND SMBus LOW-POWER I/O EXPANDER WITH RESET AND CONFIGURATION REGISTERS

## Slide 3: Chip Description and Key Features
8-bit I/O expander for I2C bus
  I2C to parallel port expander
  400-kHz fast I2C bus
  3 hardware address pins allow for use of up to 8 devices on I2C
  Noise filter on SCL/SDA inputs
General-purpose remote I/O expansion for most microcontroller families
At power on, the I/Os are configured as inputs
The I/Os can be programmed by I2C master to be as either inputs or outputs
  Latched outputs with high current drive maximum capability for directly driving LEDs
  Data for each input or output is kept in the corresponding input or output register
  The polarity of the input port register can be inverted with the polarity inversion register

## Slide 4: Package & Pins
Top-side marking: PD557

## Slide 5: Logic Diagram

## Slide 6: I2C Protocol Review
Two lines: the serial clock (SCL) and serial data (SDA)
  Connected to a positive supply through a pull-up resistor
Communication is initiated by a master sending a start condition
  A high-to-low transition on the SDA & the SCL input is high
After the start condition, the device address byte is sent
  Most-significant bit (MSB) first
  Followed by the data direction bit (R/W)
After receiving the valid address byte, the device having this address responds with an ACK
  A low on the SDA during the high of the ACK-related clock pulse

## Slide 7: I2C Protocol Review Cont.
Data transfer begins
  Only one data bit is transferred during each clock pulse
  Any number of data bytes can be transferred from the transmitter to the receiver
  Each byte of eight bits is followed by one ACK bit
    The transmitter must release the SDA line
    The receiver must pull down the SDA line during the ACK clock pulse
Master will stop the transmission by issuing a stop condition
  A low-to-high transition on the SDA & the SCL input is high

## Slide 8: Device Address
The address of the PCA9557 is shown as follows
R/~W: a high (1) indicates a read operation,
while a low (0) selects a write operation.

## Slide 9: Control Register & Command Byte
After the successful ACK of the address type, the bus master sends a command byte that is stored in the control register in the PCA9557
Command bytes are used to specify the operation and the internal registers that will be affected

## Slide 10: Input Port Register
Reflects the incoming logic levels of the pins
  All pins no matter whether a pin is an input or an output
  The default value is determined by the externally applied logic level

## Slide 11: Output Port Register
Shows the outgoing logic levels of the pins defined as outputs
  Bit values in this register have no effect on pins defined as inputs
  reads from this register reflect the value that is in the flip-flop controlling the output selection, not the actual pin value

## Slide 12: Polarity Inversion Register
Inverts the polarity of input pins
  If a bit in this register is set, the corresponding port pin's polarity is inverted
  If a bit in this register is cleared, the corresponding port pin's original polarity is retained

## Slide 13: Configuration Register
Configures the directions of the I/O pins
  If a bit in this register is set to 1, the corresponding port pin is enabled as an input
  If a bit in this register is cleared, the corresponding port pin is enabled as an output

## Slide 14: Write Operation

## Slide 15: Write Operation

## Slide 16: Read Operation

## Slide 17: I2C on S700

## Slide 18: Digital LED Tubes on S700